File: 20220112_keypad_LCD_testComplete

Example of using keypad and LCD for finding unknown resistor circuit.

// C++ code

#include <LiquidCrystal_I2C.h>

#include <Wire.h>

//define lcd pinouts

const int en = 2, rw = 1, rs = 0, d4 = 4, d5 = 5, d6 = 6, d7 = 7, bl = 3;

//define I2c address- change if required

const int i2c_addr = 0x27;

LiquidCrystal_I2C lcd(i2c_addr , en, rw, rs, d4, d5, d6, d7, bl, POSITIVE);

// keypad input test

#include <Keypad.h>

//define keypad

const int ROW_NUM = 4; //four rows

const int COLUMN_NUM = 4; //four columns

char keys[ROW_NUM][COLUMN_NUM] = {

{'1','2','3','A'},

{'4','5','6','B'},

{'7','8','9','C'},

{'*','0','#','D'}

};

byte pin_rows[ROW_NUM] = {9, 8, 7, 6}; //connect to the row pinouts of the keypad

byte pin_column[COLUMN_NUM] = {5, 4, 3, 2}; //connect to the column pinouts of the keypad

Keypad keypad = Keypad( makeKeymap(keys), pin_rows, pin_column, ROW_NUM, COLUMN_NUM );

//define string variable used to pass keypress value

String inputString;

String msg1 =" ";

String msg2 =" ";

//define integer to to hold keypress value

long inputInt = 1;

//define pins from Arduino that will be used as input to mux

int LED1 = 10;  // mux input En

int LED2 = 11;  // mux input A0

int LED3 = 12;  // mux input A1

// Define Analog inputs

#define ANALOG_IN_PIN A0  //reads Rx

// Floats for ADC Voltage & Input voltage

float adc_voltage = 0.0;

float in_voltage = 5.0;

// floats for resistance values in divider network in ohms

float R1 = 198.8;

float R2 = 1991.0;

float R3 = 21810.0;

float R4 = 220900.0;

// unkown resistor value

float Rx = 0.0;

//Float for reference voltage

float ref_voltage = 5.0;

float Res = (ref_voltage/1024);

// Float for voltage drops across Rx and R1

float ERx = 0.0;

float ER1 = 0.0;

//float for total current through resistor divider network

float IT = 0.0;

//Int for ADC value

int adc_value = 0;

// define string vriable to hold range values

String RANGE;

float rangeValue = 0.0;

//-------------------------------------------------------------------------------

void setup(){

// define pins to LEDS as outputs

pinMode(LED1,OUTPUT);

pinMode(LED2,OUTPUT);

pinMode(LED3,OUTPUT);

// set Enable for mux decoder

digitalWrite(LED1,HIGH);

// setup serial monitor

Serial.begin(9600);

// setup for LCD

lcd.begin(16,2);

lcd.backlight();

lcd. setCursor(0,0);

lcd.print("testing!...");

delay (2000);

lcd.clear();

}

//-----------------------------------------------------------------------

// get input from keypad

void loop(){

inPutkey();

readDecoder();

readAnalogpin();

overRange();

printResults();

inPutkey();

}

//------------------------------------------------------------------------

void inPutkey(){

char key = keypad.getKey();

if (key >= '0' && key <= '4') {     // only act on numeric keys

inputString = key;               // append new character to input string

inputInt = inputString.toInt(); // YOU GOT AN INTEGER NUMBER

inputString = "";               // clear inputString

//select mux channel using inputInt

if (inputInt == 1){       // range 1 selected 200 ohms

digitalWrite(LED2,LOW); //AO off

digitalWrite(LED3,LOW); //A1 off

inputString ="200 Ohms";

displayRange(); // call displayRange routine

}

else {

if (inputInt == 2){       // range 2 selected 2K ohms

digitalWrite(LED2,HIGH); //AO on

digitalWrite(LED3,LOW); //A1 off

inputString = "2K Ohms";

displayRange();

}

else {

if (inputInt == 3){       // range 3 selected 20K ohms

digitalWrite(LED2,LOW); //AO off

digitalWrite(LED3,HIGH); //A1 on

inputString = "20K Ohms";

displayRange();

}

else {

if (inputInt == 4){       // range 4 selected 200K ohms

digitalWrite(LED2,HIGH); //AO off

digitalWrite(LED3,HIGH); //A1 on

//Serial.println("selected range is = 200K");

inputString = "200K Ohms";

displayRange();

}

}

}

}

}

}

//--------------------------------------------------------------------------------

void displayRange(){

lcd.setCursor(0,0);

lcd.print("selected range");

lcd.setCursor(0,1);

lcd.print(" is = " + inputString);

Serial.println("selected range is = " + inputString);

delay(2000);

lcd.clear();

inPutkey();

}

//------------------------------------------------------------------------------

//---------------- function void readDecoder()---------------------------

void readDecoder(){

// read digital pins 11 & 12 to determine what range value to use

if ((digitalRead(LED2)== LOW) && (digitalRead(LED3) == LOW)) {

RANGE = "200";

rangeValue = R1;

}

else

if ((digitalRead(LED2)== HIGH)&&(digitalRead(LED3) == LOW)){

RANGE="2k";

rangeValue = R2;

}

else

if ((digitalRead(LED2)== LOW)&&(digitalRead(LED3) == HIGH)){

RANGE="20k";

rangeValue = R3;

}

else

if ((digitalRead(LED2)== HIGH)&&(digitalRead(LED3) == HIGH)){

RANGE="200k";

rangeValue = R4;

inPutkey();

}

}

//-------------------------------------------------------------------------

//-------------------function readAnalogpin()-----------------------------

void readAnalogpin(){

//set external reference voltage to 4.096 V

//analogReference(EXTERNAL);

analogReference(DEFAULT);

// read voltage at pin A0 5 times for precision

for (int i= 0; i<5; i++) {

adc_value = analogRead(ANALOG_IN_PIN);

delay(10);

}

//Determine voltage across Rx

adc_voltage =(adc_value * Res);

// determine is adc measurement is within 1% of calculated valve of RX

//calculate curent IT through circuit

ER1 = in_voltage - adc_voltage;

IT= (ER1)/(rangeValue);

// current thru R2 = current thru Rx because they are in series

//calculate Rx value in ohms

ERx = adc_voltage;

Rx = ERx/IT;

inPutkey();

}

//------------------------------------------------------

//----------function overRange()----------------------------

void overRange(){  // callsubroutine to check for over range

switch (inputInt) {

case 1:

if ((Rx > R1) && (Rx <= 2000)){

msg1= "2k";

msg2= "Over ";

}

break;

case 2:

if ((Rx > R2) && (Rx <= 20000)){

msg1= "20k";

msg2= "Over ";

}

else

if (( Rx < R2) && (Rx <= 200)){

msg1= "200";

msg2= "Under ";

}

break;

case 3:

if ((Rx > R3) && (Rx <= 200000)){

msg1= "200k";

msg2= "Over ";

}

else

if ((Rx < R3) && (Rx <= 2000)){

msg1= "2k";

msg2= "Under ";

}

break;

case 4:

if (( Rx < R4) && (Rx <= 20000)){

msg1= "2k";

msg2= "Under ";

}

break;

}

if (msg1 != " ") {

lcd.setCursor(0,0);

lcd.print(msg2+"range");

lcd.setCursor(0,1);

lcd.print("select "+msg1);

Serial.print(msg2 + "range..> Select \t");

Serial.print(msg1);

Serial.print(" Ohms range");

msg1 = " ";

msg2 = " ";

delay(2000);

lcd.clear();

}

for (int i = 0; i <= 4; i++) {

Serial.print("\n");

delay(10);

inPutkey();

}

}

//--------------------------------------------------------------------------

//-----------------------function void printResults()-----------------------

void printResults(){

lcd.setCursor(0,0);

lcd.print("Range is " + RANGE);

Serial.println("Range is " + String(RANGE));

lcd.setCursor(0,1);

lcd.print("adc_value = "+ String(adc_value));

delay(2000);

lcd.clear();

Serial.print("adc_value = \t ");

Serial.println(adc_value);

lcd.setCursor(0,0);

lcd.print("adc_volts = " + String(adc_voltage));

lcd.setCursor(0,1);

lcd.print("IT = "+ String(IT,5) +" Amps");

delay(2000);

lcd.clear();

Serial.println("adc_voltage = " + String(adc_voltage,5)+ " volts");

Serial.println("Total current = " +String(IT,8) + " amps" );

Serial.print("Ref_voltage = \t" +String(ref_voltage,4));

Serial.println("\n");

lcd.setCursor(0,0);

lcd.print("unknown value is");

lcd.setCursor(0,1);

lcd.print(String(Rx) + " Ohms");

delay(2000);

Serial.println(" the value of unknown ");

Serial.print("Resistor Rx is \t");

Serial.print(Rx);

Serial.println(" \t Ohms");

Serial.println("");

IT=0;

adc_value=0;

ERx =0;

ER1 =0;

//Short delay

//delay(3000);

lcd.clear();

inPutkey();

}

//-end program------------------------------------------------------------------------