// C++ code

// Flowmeter pulse & battery check test 6/13/22

// freq gen. output to Arduino Interrupt pin 2

#define flowPin 2         // input from Frq Gen simulating Pulses from Water Flow Meter

#define batVolts A0                        // analog input to measure battery voltage

int LowVoltageAlarm = 7;                 // led pin 7, used to control LED

float battVoltFloat = 0.0;               // hold value of input from analog A0, battery voltage

int battVoltRaw = 0;                     // holds map value in int form

volatile unsigned long flowRate;         // displays pulse counts

volatile unsigned long count = 0;        // holds counts from from freq generator

volatile unsigned long interval = 1000;  // timer interval, 1000ms = 1 second,

unsigned long currentTime = 0;           // hold current millis() time in milli seconds

//___________________________________________________________________

void setup(){

Serial.begin(19200);    // Debugging only

pinMode(batVolts,INPUT);              // analog input for battery voltage

pinMode(flowPin, INPUT_PULLUP);       // pin 2, pulled high with 10k resistor

pinMode(LowVoltageAlarm, OUTPUT);     //pin 7

digitalWrite(LowVoltageAlarm, LOW);    // intialize, turn off LED by setting it LOW

// Attach interrupt to run ISR for encoder to increment counts during the 1 sec interval

attachInterrupt(digitalPinToInterrupt(flowPin),Flow, RISING);

}

//___________________________________________________________________

void loop() {

if (millis() > currentTime + interval)

{

currentTime = millis();

flowRate = count/2;

Serial.print("Water Flow Rate = ");

Serial.print(flowRate);

Serial.println(" Pulses/sec");

count = 0; // reset pulse counter after counts have been read, and calculated

batteryCheck();       //  check for low battery

}

}

//______________________________________________________________________

void Flow()

//routine to count pulses from flow meter

{

count = count +1;

}

//______________________________________________________________________

void batteryCheck()

{

battVoltRaw = map(analogRead(batVolts),0,1023.0, 0, 42);

float battVoltFloat = battVoltRaw/10.0; // conver int to floating point

Serial.print(" Battery voltage: ");

Serial.println(battVoltFloat,2);

if (battVoltFloat <= 2.5)

{

digitalWrite(LowVoltageAlarm, HIGH); //turns on led if bettery is low

Serial.println(" Warning ,....Battery low!");

}

else

digitalWrite(LowVoltageAlarm, LOW); //turns off led

delay(2000); // delay long enough to see the led is on in alarm

}